## Slide 1: Xilinx Virtual Cable 2014.3
Premduth Vidyanandan & Adrian Hernandez

## Slide 2: Overview
Xilinx Virtual Cable (XVC) provides a means to program and debug your FPGA design without using a USB or parallel configuration cable. This capability helps facilitate programming and debug of systems that:
  Have an FPGA in an inaccessible location
  Require remote programming and debug of an FPGA
  Do not have direct access to the FPGA pins – e.g. the JTAG pins are only accessible via a local processor interface

## Slide 3: Key Features
XVC is an internet-based protocol that acts like a JTAG cable
Extensible to allow for safe, secure connections
Debug and programming via Vivado hardware manager

## Slide 4: System Block Diagram

## Slide 5: System Connection Flow

## Slide 6: Vivado TCL: open_hw_target
New option added to open_hw_target
  open_hw_target –xvc_url <url>
Operation Details:
  Option will open the target using the current_hw_server
  Once opened, get_hw_targets shows the XVC target
  XVC connection is closed when disconnect_hw_server is called, user will need to call open_hw_target to open connection back up
  If hw_server already has an xvc_target open, then the xvc_target will be discovered like any other cable

## Slide 7: Initializing hw_server with xvc connection
When hw_server is initialized with an XVC connection Vivado discovers the cable just like any USB cable
Start hw_server with these arguments
    hw_server -e "set auto-open-servers xilinx-xvc:localhost:10200”
The argument to the auto-open-servers argument is as follows
  xilinx-xvc:<xvc_ip/name>:<xvc_port>

## Slide 8: Debugging XVC
XVC can be debugged by launching hw_server with the following arguments:
    hw_server –L- -e "set xvc-log-level 1“
The “-e” argument sets the XVC log level
Log data is controlled through the –L

## Slide 9: For more information…
Main XVC page:
  http://www.xilinx.com/products/intellectual-property/xvc.htm
Vivado Programming and Debug User Guide
  http://www.xilinx.com/support/documentation/sw_manuals/xilinx2014_3/ug908-vivado-programming-debugging.pdf